## Slide 1: Synthesizing Electrocardiogram (ECG) from Photoplethysmogram(PPG) using Generative Adversarial Networks Paper Authors: Pritam Sarkar, Ali Etemad
Presented by:
Sri Sruthi Chilukuri
San Jose State University

## Slide 2: ECG and PPG
Electrocardiogram commonly known as ECG is an electrical procedure that captures the activity of a functioning heart.
Photoplethysmogram(PPG) is a technique which can measure just the blood volume changes under the skin.
Currently, very few wearable devices have ECG monitoring embedded in them.

## Slide 3: What’s all about CardioGAN?
To address the problem of unavailability of continuous ECG monitoring.
A CycleGAN based architecture; trained in an unpaired manner.
Attention mechanism in generators
Multiple discriminators
Both time and frequency domains are manifested.

## Slide 4: Proposed Architecture of CardioGAN

## Slide 5: Experimental setup
Data Gathering and preparation:
ECG-PPG datasets that were used were BIDMC, CAPNO, DALIA, WESAD.
Each of them had varying attributes, different patient records and even different sampling frequencies.
Followed a multi-corpus approach.
Band pass filters were applied .
Min-Max normalization over signal data to introduce homogeneity.

## Slide 6: Model architecture
GENERATOR
Attention U-Net architecture was used as generator.
Encoder contains 6 blocks with various sized filters.
Layer normalization was applied.
LeakyReLu activation function
Decoder contains similar architecture with Relu on de-convolution layers.

## Slide 7
2. DISCRIMINATOR
Dual discriminators were used to classify data in time and frequency domains.
Each of 4 convolution layers is followed by normalization layer.
LeakyReLu activation function was used except for first layer.
Single channel convolution layer as output

## Slide 8: Model Training
CardioGAN trained on Nvidia RTX GPU using TensorFlow.
80-20% train and test split on all four datasets.
CardioGAN trained in unpaired manner by shuffling ECG and PPG data.
Adam optimizer was used to train generators and discriminators.
Total training: 15 epochs.

## Slide 9: Performance evaluation

## Slide 10: Failed cases:
Few PPG signals input to the model had very pure quality.
Highly noisy PPG inputs generate ECG signals of very low quality.

## Slide 11: Future work
Generated ECG signals’ usage can be widened.
Multi-lead ECG can be further studied to extract more cardiac information.
Information that cannot be read by single channeled PPG signals can be extracted.

## Slide 12: The overall quality of the paper:
Straightforward approach
Details about CardioGAN were well described.
More graphical representations of the several architectural layers could have been provided.

## Slide 13: Critique, Future directions and suggestions:
Impact of low-quality inputs could have been discussed in detail.
This experiment has the potential to impact the medical field in a positive way.
A low-cost solution is of utmost necessity in such a scenario whether in the form of wearable devices or compact devices.
This model can be integrated with a wearable device like a wristwatch to put to real-time use to test its authenticity and reliability.

## Slide 14: References
“CardioGAN: Attentive Generative Adversarial Network with Dual Discriminators for Synthesis of ECG from PPG” by Pritam Sarkar, Ali Etemad, 30 Sept 2020; https://arxiv.org/abs/2010.00104
Thank You.